Modeling Geomagnetic Disturbances Using Computer-Based Simulations
Nikhil Nayak

---
What is a Geomagnetic Disturbance (GMD)?
Space Weather
But what does that actually mean?
- A GMD is created from magnetic field emitted by the sun, causing Geomagnetic Induced Currents (GICs)
- When the GICs collides with the Earth’s magnetic field, it can cause disturbances in electrical systems in the affected areas
- These disturbances can include the fluctuation in the system’s voltage and current, which can overheat the system and cause power outages

---
Diagram of GMDs

---
Why should you care about this?
This is a real issue, not just a theoretical problem. Take the Hydro-Quebec 1989 power outage, for example.
- On March 12, 1989, voltage fluctuations were seen on the Hydro-Quebec power grid
- One day later, the Earth’s magnetic field started violently fluctuating, causing a province-wide blackout in less than one minute
- This was caused by a solar storm that astronomers witnessed on March 10, 1989, a storm that affected dozens of countries, from Canada to Europe

---
How can we solve this?
- We need to take our geomagnetic field recordings and use them to determine the geoelectric fields at the Earth’s surface
- To understand the system we’re looking at, we need to model it
- In this case, we can use a set of mathematical equations to model the GMD system

---
Simulating a GMD
- Before we try to model a real dataset, we can start with a simulated base case. Our dataset can be defined by B(t):

---
Discretization
- Because we are implementing our model on a computer, we need to discretize the function into bins using a Fourier Transform

---
Discretization (Explained)
- FFTs are representations of a function using just sin and cos
- Each line of an FFT represents 1 function. When all the functions are added together, they resemble the original function
- This converts our data from the time domain to the frequency domain, making it easier to process the signals
Inverse FFT
FFT

---
Complex Numbers in FFTs
- To accurately represent a signal, you need to represent amplitude and phase
- Complex numbers are inherently good at representing waves because of Euler’s formula:
- Euler’s formula helps simplify the process of creating Fourier Transforms, making it possible to represent a wave using the sum of cos and sin functions
- Each complex number is just a real and imaginary component, or a x and y. x and y can make up a point on a plane, meaning the point can have a distance from origin (amplitude) and rotation from a horizontal line (phase)

---
Modeling the System
How are we going to model a GMD system?
- To model the GMD system, we are using a 5 layer model designed for the Hydro-Quebec incident. This model was created in the Boteler 2019 research paper. Here’s the model:
- To understand what all those letters mean, we’re going to need some more info

---
Modeling the System (cont.)
- K is a recursive function, defined by the base case on the right
- The 5 layer model represents 5 layers of the Earth, from 15km to 200km
- When we use layer “1”, the recursive function calls each layer until it hits the base case, returning the modeled data.

---
Relevant Model Code (Julia)

---
Benchmark
- To benchmark our computer implementation of the Boteler 2019 model, we can run some test cases

---
TABLE 3. Transfer function K(f) for the frequencies in the synthetic test
magnetic field variation for a multi-layer Earth (5-layer Québec model).
Boteler 2019 Results
Computer Implemented Results
m fm Amplitude Phase
1 | 0.000093 | 0.219701 | 77.139393
2 | 0.000208 | 0.447422 | 73.771382
3 | 0.000476 | 0.867800 | 67.172638
4 | 0.001111 | 1.539096 | 62.080986
5 | 0.002381 | 2.593561 | 60.575656
6 | 0.005556 | 4.662704 | 54.969143
7 | 0.025000 | 9.604690 | 44.381495

---
TABLE 7. Parameters of electric field waveform for a multi-layer Earth
(5-layer Québec model).
1 | 0.000093 | 43.940296 | 87.139393
2 | 0.000208 | 40.267957 | 93.771382
3 | 0.000476 | 26.033997 | 97.172638
4 | 0.001111 | 26.164632 | 102.080986
5 | 0.002381 | 20.748486 | 110.575656
6 | 0.005556 | 16.319466 | 114.969143
7 | 0.025000 | 9.604690 | 114.381495
Boteler 2019 Results
Computer Implemented Results
m fm Amplitude Phase

---
TABLE 7. Parameters of electric field waveform for a multi-layer Earth
(5-layer Québec model).
1 | 0.000093 | 43.940296 | 87.139393
2 | 0.000208 | 40.267957 | 93.771382
3 | 0.000476 | 26.033997 | 97.172638
4 | 0.001111 | 26.164632 | 102.080986
5 | 0.002381 | 20.748486 | 110.575656
6 | 0.005556 | 16.319466 | 114.969143
7 | 0.025000 | 9.604690 | 114.381495
Boteler 2019 Results
Computer Implemented Results
m fm Amplitude Phase

---
Real World Application
- Data from Fort Simpson, Canada
- Calculated Geoelectric fields for Fort Simpson dataset, mV/km/nT
K(f)

---
Conclusion
- In this project, a computer implementation of the Quebec 5-layer model was created
- Despite some challenges regarding creating a computer implementation of the simulation, I was able to create an accurate and efficient transfer function model
- In the future, I want to take the output of the model and calculate the actual currents and voltages in the system
- Additionally, I want to implement the 5 layer model in a performance-focused programming language; Julia had some issues with speed during development and testing due to its Just-In-Time compilation method

---
Bibliography
https://www.naes.com/news/what-is-a-geomagnetic-disturbance-and-how-can-it-affect-the-power-grid/
https://www.nasa.gov/mission_pages/sunearth/spaceweather/index.html
https://ieeexplore.ieee.org/abstract/document/8859181
https://towardsdatascience.com/fast-fourier-transform-937926e591cb#:~:text=As%20the%20name%20implies%2C%20the,)%20to%20O(NlogN)%20
http://www.librow.com/articles/article-10
https://wdc.bgs.ac.uk/catalog/format.html

---
Questions?